## Slide 1
Mars 2040 Optimization
16.888 Final Presentation
5/10/2016
Parker Vascik
Eric Ward
Sam Wald

## Slide 2: Motivation: Martian Settlement
US Space Policy and NASA’s Current Goals
  Sustainable, indefinite human presence in deep space
  Objectives of human space endeavors:
    Scientific
    Aspirational/Political
    Safe-haven for humanity
  Constraints:
    Budgetary
    Technological
Mars 2040 Settlement
Resupply Optimization
NASA, “Journey to Mars.” 2015.

## Slide 3: Problem Formulation: Objectives
Objectives
  Science Utility
    Number of Crew Hours
    Location Scientific Quality
  Cost
    Resupply Cost
      Total IMLEO
    Development Cost
      Transit Propulsion Capabilities
NASA, “Journey to Mars.” 2015.
Borowski, “7-Launch NTR Space Transportation System.” 2009.
Notes: Open Source: opensource.org
Fidelity:

## Slide 4: Problem Formulation: Variables
Design Variables
  10 Total Design Variables
  8 Discrete Variables
  2 Continuous Variables
  Propulsion Type and Isp directly effect Development Cost
  Location, Population, and Food directly affect Science Utility
Toups, “Transportation-Driven Mars Surface Operations.” 2014
Notes: Open Source: opensource.org
Fidelity:

## Slide 5: Problem Statement

## Slide 6: Modeling and Simulation: Modules

## Slide 7: Modeling and Simulation: DSM
Reordered to minimize feedback relationships

## Slide 8: Modeling and Simulation: Multidisciplinary Expansions
Two additional modules were developed to capture relevant objectives for the Mars 2040 campaign model
Advanced Technologies Development Cost
http://www.exploremars.org/
IMLEO Operational Cost
www.spacex.com
Notes: Review why these two objectives are especially important in the pre-conceptual design phase planning of a Mars campaign
Introduce the two technologies we are considering, advanced propulsion and ISRU. Cite Sydney’s thesis as a reason that we are focusing on ISRU instead of recycling techs

## Slide 9: Modeling and Simulation: Multidisciplinary Expansions
IMLEO Costs
Technology Development
New Modules

## Slide 10: Modeling and Simulation: Science Utility Module
S = science utility (interest-crew-hours)
Wi = site science interest (interest)
P = surface population (# crew)
t = time available for science activities (hours)
Investment in advanced technologies may be traded with:
  Reductions with campaign operational costs
  Enhancement in mission value (or perhaps safety)

## Slide 11: Modeling and Simulation: Development Cost Module
Investment in advanced technologies may be traded with:
  Reductions with campaign operational costs
  Enhancement in mission value (or perhaps safety)
Advanced propulsion will:
  Reduce fuel requirements for IMLEO or ISRU
  Potentially reduce transit time increasing astronaut time on Mars
  Chemical engine Isp improvements and nuclear thermal rockets are considered in this analysis
Notes: Talk about how advanced ISRU was found to be a non-started in our analysis since the time savings of more efficiency ISRU are not accounted for in our model. But, we do find that full lunar and full mars ISRU make the most efficient missions, so we need to develop that baseline technology

## Slide 12: Modeling and Simulation: Development Cost Module
Cost estimation for low Technology Readiness Level (TRL), far-term developments is a significant field of active research
The NASA Advanced Missions Cost Model (AMCM) was utilized in this research
The model is an analytic expression created from historical data of over 300 NASA advanced missions and technology development programs
Q = quantity of units produced
M = dry mass of technology in lbs
S = specification of technology
IOC = initial operating capability
B = block number of technology
D = difficulty to develop technology
Notes: Talk about limitation of amoritization of development cost over multiple mission campaign

## Slide 13: Modeling and Simulation: IMLEO Cost Module
A significant proportion of space mission costs results from initial launch cost into low earth orbit
New provider entrants into the market have provided opportunity (and uncertainty) for future IMLEO costs
The following three values were used as high, medium, and low IMLEO cost estimates in this analysis
Specific launch manifesting and impacts on operations not considered at this time.
Launch System | IMLEO Cost Estimate
Historical Baseline | $10,000/kg
Space Launch System | $7,000/kg
SpaceX Falcon Heavy | $1,600/kg

## Slide 14: Single Objective Optimization
The first attempt of wrapping the Mars 2040 campaign model in an optimizer explored two different single objective algorithms
Coordinate Search
non gradient-based
multi-dimensional steepest descent
local minimum susceptible
Genetic Algorithm
full design space coverage
unlikely to converge on local minimum
computationally intensive
www.holehouse.org
www.ewh.ieee.org
Notes: Explain that we didn’t want to go right to multi-objective optimization
The coordinate search is very good for local minimization as it is guaranteed to fined a local min, but with very complex design spaces it may not find the global min (requires multiple starting points)
GA is good for global search to identify the region of the global min. More computational expensive and not guaranteed to converge on global min

## Slide 15: Single Objective Optimization Coordinate Search
The efficiency of the coordinate search was maximized by “smoothing” the design space, or removing local minima
The design space smoothing has limited accuracy around an initial design point

## Slide 16: Single Objective Optimization Coordinate Search
The coordinate search was executed for ten initial starting points
  Numerous local maxima exist despite smoothing efforts
  1604 total function evaluations
Notes: We will compare the optimal result of the coordinate search with that of the GA in a few slides

## Slide 17: Single Objective Optimization Genetic Algorithm
The MATLAB genetic algorithm toolbox was utilized
Smoothing of the design space was not necessary
The parameters of the genetic algorithm were tuned to provide consistent convergence
The final optimizer converged in an average of 53 generations
Multiple trials were executed to ensure solution agreement

## Slide 18: Single Objective Optimization
The single objective results of the coordinate search and genetic algorithm yield very similar solutions
Coordinate Search
1604 function evaluations*
Optima value: 1.72e-4
Genetic Algorithm
2081 function evaluations†
Optima value: 1.72e-4
†for a single GA run
*for 10 coordinate search runs
Notes: Discuss how the two algorithms were validated against one another, as well as internally through multiple rounds of convergence testing (with different initial points and parameters and such)

## Slide 19: Multi-Objective Optimization

## Slide 20: Multi-Objective Optimization

## Slide 21: Final Recommendation

## Slide 22: Learnings and Future Work
Additional Variables
  Martian ISRU efficiency (ECLSS consumables, ascent prop)
  Automated plant growth systems
  Alternate sites
  Additional development costs
Additional Objectives
  Initial emplacement costs
  Risks (Technological, Operational)
Additional Sensitivities
  Development costs
    Site science interest
  Settlement time horizon

## Slide 23: Problem Formulation: Bounds and Constraints
Variable Bounds
  Current Mars information
  Theoretical limits
  Current capabilities
  Expected developments
Constraints
  Physics-based dependencies
  Mass and energy balance
  Drives system sizing
    Habitation
    Transportation
    Power
    ISRU
    ISFR
    Staging